## Slide 1: Discussion of Restart

## Slide 2: Token based restart
Token is a derived secret from the first key-management DTLS connection using a specific TLS exporter label
Restarting node
Peer node
Init: Token
Init-ACK: State cookie
Token OK
Sending response
Encoding 5-tuple in state cookie
Cookie Echo
Cookie Ack
DTLS Handshake
Validation

## Slide 3: Token based restart shortcomings
On path attacker that can capture and race Init can fail restart
  Attacker can capture token
  Attacker’s Init reach peer first
    Drop original or having shorter path from point of capture to Peer
    Change restarting port allowed?
Restarting Nodes Token that arrive after rebinding of 5-tuple expected to be dropped as token has been consumed.
Restarting node would have to do full restart -> Restarts the gNB
Restarting node
Peer node
Init: Token
Init-ACK: State Cookie
Cookie Echo
Cookie Ack
Attacker
Token OK
Sending response
5-tuple in State cookie
DTLS Handshake would fail as attacker can’t identify as expected ID.
X
SCTP Association restarted

## Slide 4: Restart with Ericsson like proposal
Generate Restart specific key-material, see next slide
Restarting side sends Init and gets back Init-Ack with Peer nodes state cookie.
Restarting sends DTLS chunk protected Cookie Echo using restart key-context
Peer Node answers using DTLS chunk using restart key
Entering Protected
Run new Key-management handshake and switch to regular key context
Restarting node
Peer node
Init:
Init-ACK:
Cookie Echo
Cookie Ack
Attacker
State Cookie restarting 5-tuple
Accept restart DTLS chunk decrypt and state cookie ok + matches 5-tuple
DTLS Handshake

## Slide 5: Ericsson Restart when integrated with updated DTLS Chunk
Key material for restart
  Make key-derivation from key-management session
  Use restart indicator in DTLS chunk combined with DTLS record with (DTLS Connection ID if used) + epoch to identify actual key for SCTP association.
Restart needs to be rekeyed also to ensure that latest re-authentication is basis for key-material

## Slide 6: Restart with Ericsson like proposal
We can’t prevent an attacker to create a trombone route through the attacker when restarting if they can on-path drop packets
If attacker only can race the restarting node’s packet then restarting node should be able to complete restart.
Need to prevent the restart to fail if the attacker lets the packets through
Restarting nodes IP address as seen from peer need to be included in state cookie to prevent attacker being able copy DTLS chunk in Cookie Echo
Restarting node
Peer node
Init:
Init-ACK:
Cookie Echo
Cookie Ack
Attacker
Init-ACK with state Cookie with attacker 5-tuple
State Cookie restarting 5-tuple
X
Reject attacker Cookie Echo due to state cookie not matching 5-tuple
Accept restart As state cookie matches 5-tuple

## Slide 7: Restart with Ericsson like proposal
Capturing State Cookie will not help as attacker lacks key context to protect Cookie Echo.
Peer Node need to be able to separate attackers with rewritten source IP/Port from restarting node’s packet. Impact on state cookie.
Address parameter per RFC 9260 rules are not allowed to be different.
  Port is part of state cookie per 9260
Restarting node
Peer node
Init:
Init-ACK:
Cookie Echo
Cookie Ack
Attacker
Init-ACK with state Cookie with attacker 5-tuple
State Cookie restarting 5-tuple
X
Reject attacker Cookie Echo due to state cookie not matching 5-tuple
Accept restart As state cookie matches 5-tuple
1
2.
3.