## Slide 1: Matching DTLS Chunk based solution against Requirements for Securing SCTP Traffic using DTLS
https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-chunk/
https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-handshake/
2023-12-01

## Slide 2: Generic Requirements
Protocol mechanisms should not limit availability of communication or result in (reliable) user message loss. (MUST)
  Pass
Signalling message sizes of at least 1 GB (0.5 MB currently in use) supported, if unlimited is not feasible. (MUST)
  Unlimited message size as in unprotected SCTP
    Without I-DATA a large message can block handshake exchange to rekey

## Slide 3: Functional Requirements for SCTP
Features from the base specification
  Ordered reliable transmission of user messages (MUST) - Pass
  Multihoming as specified in RFC 9260 (MUST) - Pass
  Dynamic address reconfiguration as specified in RFC ???? (MAY) – Proposes to not use SCTP-AUTH at all. Changed context matching
    If using SCTP-AUTH and not encrypting ASCONF chunk followed by DTLS Chunk: It will work
    If protecting ASCONF there are challenges
    Will need more discussion on how to solve it.
  Restart procedure (MUST) – Not included solutions exists: Expect to have a solution.
Parametrization
  At least two SCTP streams available to the application (MUST) Pass

## Slide 4: Implementation Considerations for SCTP
SCTP_EXPLICT_EOR (SHOULD): Not Impacted
Partial delivery (MUST): Not Impacted
User message sizes must not be limited by a protocol implementation: Not Impacted
It is implementable using an SCTP userland stack (MUST) Yes (Ericsson)
It is implementable using an SCTP kernel stack (MUST): Michael see no reason not (but not implemented yet)
It is implementable using an open source (not referring to licensing) SCTP stack (SHOULD): Appear likely
TBD: licensing

## Slide 5: Security Requirements
An on-path attacker being able to replay messages, insert messages, or modify messages is considered. (MUST): Yes have been considered
Fundamental
  Mutual authentication (MUST) Pass
  Privacy and integrity is required for user data (MUST) Pass
Best practices for long lived sessions
  Periodic re-authentication, for example allowing a certificate update (MUST) Pass
  It must the possible to run DH, for example once per hour or every 100GB. (MUST) Pass
Availability
  Replay or injection must not affect the availability of the association. (MUST) Pass
  In particular, the SCTP restart procedure must not allow to take over an SCTP association by an attacker. (MUST) Evaluation required when solution in place

## Slide 6: Implementation Considerations for DTLS
Support DTLS 1.3 (SHOULD) Yes
Support DTLS 1.2 (MAY) Possible but not intended
For some participants it is preferred to use unmodified DTLS implementations (MAY) Possible with user land stack, not for a kernel Record processing.