## Slide 1: DTLS for SCTP’ Overview solutions
https://datatracker.ietf.org/doc/draft-ietf-tsvwg-dtls-over-sctp-bis/
https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-crypto-chunk/
https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-crypto-dtls/
https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-chunk/
https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-handshake/
Magnus Westerlund
John Preuß Mattsson
Claudio Porfiri
IETF TSVWG Interim
2023-09-17

## Slide 2: IPR Declarations
draft-ietf-tsvwg-dtls-over-sctp-bis
  https://datatracker.ietf.org/ipr/5195/
  https://datatracker.ietf.org/ipr/5218/
draft-westerlund-tsvwg-sctp-crypto-chunk
  None
draft-westerlund-tsvwg-sctp-crypto-dtls
  https://datatracker.ietf.org/ipr/6180/
  https://datatracker.ietf.org/ipr/6179/
https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-chunk/
  Will be submitted
https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-handshake/
  Will be submitted (FRAND)

## Slide 3: The Proposals: DTLS over SCTP
DTLS over SCTP (DTLS/SCTP)
  https://datatracker.ietf.org/doc/draft-ietf-tsvwg-dtls-over-sctp-bis/
  https://datatracker.ietf.org/doc/draft-tuexen-tsvwg-rfc4895-bis/
An Adaptation layer between Upper Layer Protocol (ULP)
  Fragments user messages into multiple fragments
  Each fragment protected by a DTLS record
Relies on SCTP-AUTH to ensure record order
  DTLS keys the SCTP-AUTH
Uses parallel DTLS connection for rekeying
  Use DTLS Connection IDs for identification
User Message
m1
m2
m3
m4
m1'
m2'
m3'
m4'
Fragmentation
DTLS Protect
Operation
SCTP Transmission
SCTP Authentication
Plain Text
Protected User Message
SCTP Stack
DTLS/SCTP Layer
ULP
SCTP AUTH
Keys

## Slide 4: DTLS/SCTP
These slides assumes SCTP-AUTH is fixed:
  Direction dependent keying of cipher
  That DTLS/SCTP will rotate the SCTP-AUTH master key before 2^32 TSN has been protected by the same key
DTLS Replay Protection: Off
  To prevent DTLS records being delivered to adaptation layer out of order from being dropped due being out of replay window
  Normal SCTP stack implementation robustness against replay
SCTP User message limitations
  With good SCTP APIs and message tracking
    No Limit exists
  Using RFC 6458 API
    Message must not take longer time to transfer than time between re-keyings
    The limitation in setting SCTP-AUTH key to use when sending causes this limit
      Can’t rekey again until the message has concluded and the old DTLS connection is retired

## Slide 5: DTLS/SCTP: Rekeying
When necessary to rekey, initiate a new DTLS connection. Using DTLS’s connection IDs to separate the old and new DTLS Connection
  Use TLS Exporter to get a key from DTLS connection for SCTP-AUTH
Start using new DTLS connection for records and in SCTP-AUTH
  RFC 6458 API if only enables setting SCTP-AUTH key on new SCTP messages
Old DTLS Connection can’t be closed until:
  All DTLS records protected by that session have been decrypted
    Data loss if not done correctly -> Need to abort SCTP Association
  RFC 6458 API requires draining whole session to know when all has been delivered
  To avoid draining, implementation needs to
    track what DTLS session was used on which DTLS records
    know which data offsets they represent in messages
    And know when they been non-renegable ACKed

## Slide 6: DTLS/SCTP: DTLS Key Update
KeyUpdate is forbidden
  Requires the same coordination as a new DTLS connection to avoid loosing records
  Same risk for dropping the key early due to encryption and delivery order are more disconnected and related to user message fragments
Key Update do not result in a new SCTP-AUTH key
  Minor issue as HMAC-SHA 256 is strong and have a long lifetime

## Slide 7: DTLS/SCTP
Necessary cipher operations:
  Performs one set of DTLS cipher operations on each user message data fragment
  Performs SCTP-AUTH cipher operations on each SCTP packet
SCTP Restart
  SCTP-AUTH requires endpoints to maintain SCTP-AUTH’s crypto context to authenticate COOKIE-ECHO as only authenticated ones are accepted
  Then one can negotiate a new DTLS connection to protect the new user message data

## Slide 8: The Proposals: DTLS in Crypto Chunk
DTLS in SCTP (DTLS in Crypto Chunks)
  https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-crypto-dtls/
  https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-crypto-chunk/
Crypto Chunk is a new SCTP Chunk
  Encapsulated all other chunks in a crypto envelope on per SCTP packet basis
DTLS is a protection engine
  DTLS handshake messages sent as SCTP messages in DATA chunks using a specific PPID
  After DTLS keys are established all future SCTP packet’s contents are protected
  At rekeying perform handshake for a new DTLS connection
Fragmentation done by SCTP’s normal message fragmentation mechanism
DTLS Record Processing
SCTP Header Handler
SCTP Crypto Chunk Handler
SCTP Chunk Handler
DTLS Protection Engine Key-management
ULP
Keys
DTLS Handshake messages

## Slide 9: DTLS in Crypto Chunk Message Format
DCI
  Identifies the DTLS connection used for keying this DTLS record
Payload:
  Application Data DTLS record with protected chunks

## Slide 10: DTLS in Crypto Chunk
Crypto Chunk is framework that do allow other protection engines to be defined in the future
  DTLS per packet protection and key-management are still two components in the framework
Crypto Chunk requires integration of down grade attack prevention between protection engines
SCTP User Message limitations
  No limitation exist as per normal SCTP
SCTP Packet size limitations
  Per packet MTU limited by DTLS record size supported
  Maximum: 16384 bytes of plaintext chunks
Performs a single pass of AEAD cipher operations on the plain text / cipher text for encryption / decryption per SCTP packet

## Slide 11: DTLS in Crypto Chunk: Rekeying
When necessary to rekey, periodic or data limits initiate a new DTLS handshake as SCTP user messages with PPID
When keys have been derived install them for reception related to Crypto Chunk flag field DCID
When handshakes completes start using new keys
Leave old keys in place to drain network of SCTP packets protected by old key
  A MSL (2 min) timer is sufficient
  Close old DTLS connection
As soon as both sides have keys, i.e. after handshake acks one can switch
  Will at worst induce some packet loss
DTLS Key Update
  DTLS KeyUpdate message sent as user message between peers
  When KeyUpdate is ACKed by DTLS peer start using it in send direction by installing traffic secret for the DCI + Epoch
  When receiving KeyUpdate install keys for reception and ACK
  Recommend to drop old keys one MSL after first packet with new Epoch seen.

## Slide 12: DTLS in Crypto Chunk
Replay Protection
  Should be used to improve replay robustness
  DTLS can prevent any SCTP Packet from being delivered more than once
    Prevents non-data replay
  Packets outside of replay window (severely out of order) will be dropped

## Slide 13: SCTP Association Restart
DTLS Chunk
Maintained protection engine crypto context and INIT protected by Crypto Chunk
  Will work poorly due to IV construction
We will propose a better solution for secured restart

## Slide 14: The Proposals: DTLS Chunk + DTLS Key Management
SCTP DTLS Chunk Handler
DTLS in SCTP (DTLS in Crypto Chunks)
  https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-chunk/
  https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-handshake/
DTLS Chunk is a new SCTP Chunk
  Encapsulated all other chunks in a DTLS 1.3 record on per SCTP packet basis
  Performs application data DTLS record processing
  Need API to establish ciphers and traffic secrets on per DTLS Connection, Epoch and Direction
User level DTLS 1.3 used for authentication and key establishment, alerts, and Close_Notify etc.
  These DTLS messages are sent as user message with PPID = DTLS-SCTP and a DCI preamble
Fragmentation done by SCTP’s normal message fragmentation mechanism
DTLS 1.3 Record Processing
SCTP Header Handler
SCTP Chunk Handler
DTLS in SCTP Key-management
ULP
API
DTLS Handshake messages
DTLS 1.3

## Slide 15: DTLS Chunk Message Format
DCI = DTLS Connection ID
  Identifies the DTLS connection this DTLS message is intended for or a new one when carrying handshake packets
DTLS message contains one or more DTLS records with non-application data type.
DCI:
  DTLS Connection ID pointing to traffic secret to use
Payload:
  DTLS record with protected SCTP Chunks
  DTLS record contains epoch indication

## Slide 16: DTLS Chunk
Currently defines only a DTLS 1.3 based protection chunk of SCTP packet chunks
  Includes a down-grade prevention mechanism for other future protection solutions for the initial SCTP negotiation
SCTP User Message limitations
  No limitation exist as per normal SCTP
SCTP Packet size limitations
  Per packet MTU limited by DTLS record size supported
  Maximum: 16384 bytes of plaintext chunks
Performs a single pass of AEAD cipher operations on the plain text / cipher text for encryption / decryption per SCTP packet

## Slide 17: DTLS Chunk: Rekeying
When necessary to rekey, periodic or data limits initiate a new DTLS handshake as SCTP user messages with PPID
When keys have been derived install them for reception related to Crypto Chunk flag field DCID
When handshakes completes start using new keys
Leave old keys in place to drain network of SCTP packets protected by old key
  A MSL (2 min) timer is sufficient
  Close old DTLS connection
As soon as both sides have keys, i.e. after handshake acks one can switch
  Will at worst induce some packet loss
DTLS Key Update
  DTLS KeyUpdate message sent as user message between peers
  When KeyUpdate is ACKed by DTLS peer start using it in send direction by installing traffic secret for the DCI + Epoch
  When receiving KeyUpdate install keys for reception and ACK
  Recommend to drop old keys one MSL after first packet with new Epoch seen.

## Slide 18: DTLS Chunk
Replay Protection
  Should be used to improve replay robustness
    Especially for non-DATA chunks
  DTLS can prevent any SCTP Packet from being delivered more than once for SCTP chunk processing
  Packets outside of replay window (severely out of order) will be dropped

## Slide 19: DTLS Chunk Abstract API
Get Supported Ciphers
Set Traffic secrets
  Per DTLS Connection ID set cipher
  Per DTLS Connection ID (DCI), epoch and direction set traffic secret
Destroy Traffic Secrets
  Remove secrets per DCI and epoch
Set DCI and Epoch to use for protection of SCTP packets sent
Configure Replay Protection window
Access information or configure alerts per DTLS Connection and epoch
  Cipher Invocations
  Failed verifications
Indication of first packets with new Epoch received

## Slide 20: SCTP Association Restart
DTLS Chunk
Maintained protection engine crypto context and INIT protected by Crypto Chunk
  Will work poorly due to IV construction
We will propose a better solution for secured restart