## Slide 1: DTLS based Security for SCTP Report from Design Team
2024-02-23

## Slide 2: Design Team Participants
Marcelo Ricardo Leitner
Xin Long
John Mattsson
Claudio Porfiri
Tirumaleswar Reddy.K
Zahed Sarker
Hannes Tschofenig
Michael Tüxen
Magnus Westerlund

## Slide 3: Requirements
The Design Team discussed before New Year what was perceived as the requirements to fulfill 3GPPs needs
Presented at IETF 118 in TSVWG session:
  https://datatracker.ietf.org/meeting/118/materials/slides-118-tsvwg-sessb-3-tsvwg-design-team-to-set-requirements-for-dtlssctp
Further discussed and assigned importance:
  https://github.com/sctplab/sctp-dtls-requirements/blob/main/SCTP_DTLS_REQ.pptx

## Slide 4: The Proposals on the Table
A: DTLS over SCTP based on RFC 6083 proposed by Ericsson
  https://datatracker.ietf.org/doc/draft-ietf-tsvwg-dtls-over-sctp-bis/
  https://datatracker.ietf.org/doc/draft-ietf-tsvwg-rfc4895-bis/
B: DTLS Chunk alternative solution proposed by Ericsson
  https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-chunk/
  https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-handshake/
C: Michael Tüxen’s and Hannes Tschofenig’s DTLS over SCTP proposal
  https://datatracker.ietf.org/doc/draft-tuexen-tsvwg-rfc6083-bis/
  https://datatracker.ietf.org/doc/draft-tuexen-tsvwg-sctp-ppid-frag/
  https://datatracker.ietf.org/doc/draft-ietf-tsvwg-rfc4895-bis/
  https://datatracker.ietf.org/doc/draft-tschofenig-tls-extended-key-update/
  RFC 9261 for periodic Authentication

## Slide 5: Analysis
All three solution proposals meets the Design Team’s agreed technical requirements:
  https://github.com/sctplab/sctp-dtls-requirements/blob/main/SCTP_DTLS_REQ-matching-dtls-over-sctp-westerlund.pptx
  https://github.com/sctplab/sctp-dtls-requirements/blob/main/SCTP_DTLS_REQ-matching-dtls-chunk.pptx
  https://github.com/sctplab/sctp-dtls-requirements/blob/main/SCTP_DTLS_REQ-matching-dtls-over-sctp-tuexen.pptx
The proposals differs in:
  Some Technical Details and properties
  IPR claims and impact on open source SCTP implementations
  Expected time to complete the work in IETF

## Slide 6: Completion Time
A - DTLS over SCTP per Ericsson’s proposal:
  All work is TSVWG internal
  SCTP-AUTH needs to be completed
  Specifications expected to be ready for publication request by end of 2024
B - DTLS Chunk:
  All work is TSVWG internal
  Specifications expected to be ready for publication request by end of 2024
C - DTLS over SCTP proposal by Tüxen et al
  Dependent on adopting one technical function (key-update) into TLS WG
    Key-update has general use not only for DTLS for SCTP
  SCTP-AUTH needs to be completed
  TSVWG documents expected to be ready for publication by end of 2024
  Assuming adoption the Key Updated in TLS WG is expected time to be ready for publication request is at least 2 years

## Slide 7: IPR
A - DTLS over SCTP per Ericsson’s proposal:
  Two IPR disclosures (RAND): https://datatracker.ietf.org/ipr/5195/ https://datatracker.ietf.org/ipr/6218/
B - DTLS Chunk:
  draft-westerlund-tsvwg-sctp-dtls-chunk: https://datatracker.ietf.org/ipr/6219/
    Defensive declaration with option of RAND (see disclosure)
  draft-westerlund-tsvwg-sctp-dtls-handshake:
    RAND license: https://datatracker.ietf.org/ipr/6220/
C - DTLS over SCTP proposal by Tüxen et al
  No IPR disclosures

## Slide 8: IPR Implications
Two RAND license applying to implementation on top of a SCTP stack of DTLS for SCTP
Two different parts:
  Defensive Declaration with option of RAND on implementation that ends up inside SCTP stack, the license is attempting to not impact kernel open source
  A RAND license for the Rekeying implementation on top of the SCTP stack
Currently no IPR disclosure

## Slide 9: A - DTLS over SCTP based on RFC 6083 proposed by Ericsson
Depending on DTLS 1.3 features
  DTLS Connection IDs
    Could be engineered around with an DTLS record encapsulation layer
Rekeying issue
  Knowing when an old DTLS connection and its SCTP-AUTH key are no longer required
  Interaction with SCTP-AUTH API that limits when key can be replaced
Beyond SCTP-AUTH all on top of SCTP Stack
Relies on SCTP stack for any replay protection
Two crypto passes:
  DTLS over ULP User Messages
  SCTP-AUTH over SCTP Packet Chunks

## Slide 10: B - DTLS Chunk alternative solution proposed by Ericsson
One DTLS record per SCTP packet
  Simple rekeying
  Uses DTLS record size that are common in other DTLS applications
  DTLS Replay protection prevents SCTP stack having to process replayed old packets
  Single Crypto operation pass
Encrypts SCTP protocol as well as ULP Data
DTLS record processing integrated into SCTP stack
  Kernel SCTP implementations require split DTLS implementation
Maximum SCTP Payload MTU: 16384 bytes
  Can be increased to 64 KB by DTLS Record size change (draft-mattsson-tls-super-jumbo-record-limit-00) (Optional improvement for large MTUs)

## Slide 11: C - Michael Tüxen’s and Hannes Tschofenig’s DTLS over SCTP proposal
Fragments ULP user messages into multiple SCTP messages
  Requires in-order reliable delivery on streams
  Enables I-Data like interleaving between streams of ULP user messages
  Does not work with partial reliability messages (RFC 3758)
Re-authentication based on RFC 9261
  Cloudflare have implementations, none currently open source
  Implementations are not particular large, one no more than ~300 lines
Relies on SCTP stack for any replay protection
Two crypto passes:
  DTLS over ULP User Messages
  SCTP-AUTH over SCTP Packet Chunks

## Slide 12: Choosing a Solution
The main choice is between timely completion and potentially IPR free
  3GPP has stressed in their LSes timely completion:
    RAN3: ACTION: RAN3 asks IETF TSVWG group to take the above into account and expedite the discussion so that a solution which does not limit the maximum message size is selected as soon as possible.
    SA3: ACTION: SA3 kindly asks IETF Transport Area Working Group (TSVWG) to take the above information into account and expedite the decision process so that a solution is ready by the envisioned time.
For timely completion choose between type of SCTP stack impact:
  DTLS Chunk: DTLS Chunk and potential split DTLS implementation
  DTLS over SCTP per Ericsson: SCTP-AUTH and potentially improved API to solve rekeying ambiguities
Else
  DTLS over SCTP per Tüxen et al

## Slide 13: Summary Slide (Table)
Options | Drafts | WGs involved | IPRs | Time estimation | Implementation aspects
Option A | https://datatracker.ietf.org/doc/draft-ietf-tsvwg-dtls-over-sctp-bis/ https://datatracker.ietf.org/doc/draft-ietf-tsvwg-rfc4895-bis/ | TSVWG | Two IPR disclosures (RAND) | By end of 2024 | No IPR claim on SCTP part Major dependencies on implementation on top of SCTP stack
Option B | https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-chunk/ https://datatracker.ietf.org/doc/draft-westerlund-tsvwg-sctp-dtls-handshake/ | TSVWG | Two IPR disclosures (Defensive + RAND) | By end of 2024 | 1 Defensive IPR on SCTP part DTLS record processing integrated into SCTP stack SCTP kernel stack required split DTLS implementation
Option C | https://datatracker.ietf.org/doc/draft-tuexen-tsvwg-rfc6083-bis/ https://datatracker.ietf.org/doc/draft-tuexen-tsvwg-sctp-ppid-frag/ https://datatracker.ietf.org/doc/draft-ietf-tsvwg-rfc4895-bis/ https://datatracker.ietf.org/doc/draft-tschofenig-tls-extended-key-update/ RFC 9261 for periodic Authentication | TSVWG, TLS | 0 IPR disclosures | By end of 2024 at TSVWG By end of 2025 at TLS | Full solution can be implemented license free. Same split as A between SCTP stack and SSL/TLS libraries. Does not support partial reliability over 16384 bytes

## Slide 14: WG Question