## Slide 1: Matching DTLS over SCTP against Requirements for Securing SCTP Traffic using DTLS
https://datatracker.ietf.org/doc/draft-tuexen-tsvwg-rfc6083-bis/

## Slide 2: Generic Requirements
Protocol mechanisms should not limit availability of communication or result in (reliable) user message loss. (MUST) Draining if messages from epoch n - 1 are still in process when switching to epoch n + 1. This is very unlikely. This uses accounting for SCTP AUTH keys in the SCTP layer.
Signalling message sizes of at least 1 GB (0.5 MB currently in use) supported, if unlimited is not feasible. (MUST) User messages not limited to an epoch, if PPID based fragmentation is used. Not sure if this is wise…

## Slide 3: Functional Requirements for SCTP
Features from the base specification
  Ordered reliable transmission of user messages (MUST) Yes, using PPID based fragmentation
  Multihoming as specified in RFC 6260 (MUST) Yes.
  Dynamic address reconfiguration as specified in RFC 5061 (MAY) Yes.
  Restart procedure (MUST) Yes.
Parametrization
  At least two SCTP streams available to the application (MUST) Yes.

## Slide 4: Implementation Considerations for SCTP
SCTP_EXPLICT_EOR (SHOULD) Not needed for PPID-based fragmentation.
Partial delivery (MUST) Yes, but not needed at the SCTP layer. Needs to be done above DTLS.
User message sizes must not be limited by a protocol implementation Yes, for ordered reliable messages.
It is implementable using an SCTP userland stack (MUST) Yes.
It is implementable using an SCTP kernel stack (MUST) Yes.
It is implementable using an open source (not referring to licensing) SCTP stack (SHOULD) Yes.
TBD: licensing As far as authors are affected: no IPR.

## Slide 5: Security Requirements
An on-path attacker being able to replay messages, insert messages, or modify messages is considered. (MUST) Yes.
Fundamental
  Mutual authentication (MUST) Yes.
  Privacy and integrity is required for user data (MUST) Yes.
Best practices for long lived sessions
  Periodic re-authentication, for example allowing a certificate update (MUST) Yes using draft-tschofenig-tls-post-handshake.
  It must the possible to run DH, for example once per hour or every 100GB. (MUST) Yes using draft-tschofenig-tls-extended-key-update
Availability
  Replay or injection must not affect the availability of the association. (MUST) Done using SCTP AUTH.
  In particular, the SCTP restart procedure must not allow to take over an SCTP association by an attacker. (MUST) Done using SCTP AUTH or draft-tuexen-tsvwg-sctp-restart-token (to be submitted).

## Slide 6: Implementation Considerations for DTLS
Support DTLS 1.3 (SHOULD) Yes.
Support DTLS 1.2 (MAY) Problematic due to limited number of epochs. The rest could be adapted.
For some participants it is preferred to use unmodified DTLS implementations (MAY) Possible, if the DTLS implementation supports DTLS/SCTP… Which means: No.