## Slide 1: Requirements for Securing SCTP Traffic using DTLS draft-tuexen-tsvwg-sctp-dtls-req-00
Michael Tüxen (tuexen@fh-muenster.de), Editor

## Slide 2: Design Team Participants
Marcelo Ricardo Leitner
Xin Long
John Mattsson
Claudio Porfiri
Tirumaleswar Reddy.K
Zahed Sarker
Hannes Tschofenig
Michael Tüxen
Magnus Westerlund

## Slide 3: Functional Requirements for SCTP
Features from the base specification
  Ordered reliable transmission of user messages
  Multihoming but no dynamic address reconfiguration
  Restart procedure
Parametrization
  At least two streams
  User message sizes of at least 1 GB (0.5 MB currently in use) supported
Constraints
  Protocol mechanisms should not limit availability of communication

## Slide 4: Implementation Considerations for SCTP
User message sizes must not be limited by a protocol implementation
For some participants it is preferred to be able to use open-source kernel SCTP implementations

## Slide 5: Security Requirements
Mutual authentication must be used with periodic re-authentication allowing a certificate update
It must the possible to run DH once per hour or every 100GB.
Privacy and integrity is required for user data.
An on-path attacker being able to replay messages, insert messages, or modify messages must not be able to affect the availability of the association or change user data.
In particular, the SCTP restart procedure must not allow to take over an SCTP association by an attacker.

## Slide 6: Implementation Considerations for DTLS
Focus on DTLS 1.3
For some participants it is preferred to use unmodified DTLS implementations